## Slide 1: Computer Networks
Vijay Kumar Chaurasiya

## Slide 2: What is a computer network?
It is an interconnection of autonomous devices.
Interconnection: able to exchange meaningful information. (Protocols).
Autonomous: do not control each other (independent)
Devices: Any computing device eg. Computer, laptop, mobile…..

## Slide 3: What are the type of network?
Point to point network: communication link will be used by the two peers only
Multipoint Network (Shared Network): nodes are sharing communication link
A
B
C
D
E

## Slide 4: Other Classification
Based on the communication medium we can classify a network as:
  Wired network
  Wireless network
Based on the span of the network we can classify a network as:
  PAN (1 -10mts)
  LAN (1 km – 10 kms)
  MAN(10 kms – 100 kms)
  WAN(more than 100 Kms)

## Slide 5: What are the advantages of Computer Networks?
Resource and data sharing
Resources: Hard disk space, RAM, Printer, CD/DVD-Drive, any other hardware connected to the host.
Data Sharing: File sharing, chat (voice / Video)….
Distributed processing
Parallel processing
Eg. Cloud Computing:
  Infrastructure as service
  Software as service
  Computing as service

## Slide 6: Disadvantages?
Privacy
All kind security attack on hosts are possible over the network. Eg. Man in middle attack, Denial of service attack, data stealing etc.

## Slide 7: Important Terms
Packet Switching (Analogous to Postal Service)
Circuit Switching (Analogous to Telephone Service)
Over Packet Switching Network we can have
  Connection Less service
  Connection Oriented service

## Slide 8: Motivation of Layering
Preparing data for successful and meaningful communication was a big programming task because it has the following problems:
  Hardware failure
  Network congestion
  Packet delay or loss
  Data corruption
  Data duplication or inverted arrivals

## Slide 9: Solving The Problem
To solve big problem:
  Divide the problem into pieces
  Solve sub problems separately
  Combine into integrated whole
  Result is layered protocols
Protocol Layering
  Separates protocol functionality
  Each layer solves one part of the communication problem
  Intended primarily for protocol designers
  Set of layers is called a protocol stack

## Slide 16
OSI = Open Systems Interconnection: deals with open systems, i.e. systems open for communications with other systems.
Specified in ISO 7498.
Model has 7 layers.
OSI Reference Model
Notes: The OSI model describes the flow of data in a network, from the lowest layer (the physical connections) up to the layer containing the user’s applications. Data going to and from the network is passed layer to layer. Each layer is able to communicate with the layer immediately above it and the layer immediately below it. This way, each layer is written as an efficient, streamlined software component. When a layer receives a packet of information, it checks the destination address, and if its own address is not there, it passes the packet to the next layer.
When two computers communicate on a network, the software at each layer on one computer assumes it is communicating with the same layer on the other computer. For example, the Transport layer of one computer communicates with the Transport layer on the other computer. The Transport layer on the first computer has no regard for how the communication actually passes through the lower layers of the first computer, across the physical media, and then up through the lower layers of the second computer.

## Slide 17: A 7- Layer ISO –OSI Model for Networking
Application Layer | High-level APIs, including resource sharing, remote file access.
Presentation Layer | Translation of data between a networking service and an application; including character encoding, data compression and encryption/decryption.
Session Layer | Managing communication sessions, i.e., continuous exchange of information in the form of multiple back-and-forth transmissions between two nodes.
Transport Layer | Reliable transmission of data segments between points on a network, including segmentation, acknowledgement and multiplexing
Network Layer | Structuring and managing a multi-node network, including addressing, routing and traffic control
Data Link Layer | Reliable transmission of data frames between two nodes connected by a physical layer
Physical Layer | Transmission and reception of raw bit streams over a physical medium
International Organization for Standardization (ISO) created the Open System Interconnection (OSI) protocol architecture starting in the late 1970s and matured by the early 1990s.

## Slide 18
Layers 1-3 are relate to communications technology.
Layers 4-7 are relate to user applications.
7-Layer OSI Model
Layer 7
Layer 6
Layer 5
Layer 4
Layer 3
Layer 2
Layer 1
Application Layer
Presentation Layer
Session Layer
Transport Layer
Network Layer
Data Link Layer
Physical Layer
Communications subnet boundary
Notes: The Application layer represents the level at which applications access network services. This layer represents the services that directly support applications such as software for file transfers, database access, and electronic mail.
· The Presentation layer translates data from the Application layer into an intermediary format. This layer also manages security issues by providing services such as data encryption, and compresses data so that fewer bits need to be transferred on the network.
· The Session layer allows two applications on different computers to establish, use, and end a session. This layer establishes dialog control between the two computers in a session, regulating which side transmits, plus when and how long it transmits.
· The Transport layer handles error recognition and recovery. It also repackages long messages when necessary into small packets for transmission and, at the receiving end, rebuilds packets into the original message. The receiving Transport layer also sends receipt acknowledgments.
· The Network layer addresses messages and translates logical addresses and names into physical addresses. It also determines the route from the source to the destination computer and manages traffic problems, such as switching, routing, and controlling the congestion of data packets.
· The Data Link layer packages raw bits from the Physical layer into frames (logical, structured packets for data). This layer is responsible for transferring frames from one computer to another, without errors. After sending a frame, it waits for an acknowledgment from the receiving computer.
· The Physical layer transmits bits from one computer to another and regulates the transmission of a stream of bits over a physical medium. This layer defines how the cable is attached to the network adapter and what transmission technique is used to send data over the cable
This partition into ‘lower’ and ‘upper’ layers is a widely used way to distinguish between the communications-oriented layers and the applications- oriented layers.
In fact layers 5 and 6 are often ignored in practical applications (the Internet protocol hierarchy has no equivalents to layers 5 and 6).

## Slide 19
Explicit Presentation and session layers missing in Internet Protocols
Data Link and Network Layers redesigned
TCP/IP vs OSI
Application
Presentation
Session
Transport
Network
Data Link
Physical
Application
TCP
IP
Network Interface
Hardware
Notes: The Physical Layer is concerned with the details of bit transmission over a physical channel.
Design issues for this layer include:
the definition of 0 and 1, e.g. how many volts represents a 1, and how long a bit lasts,
whether the channel is simplex or duplex,
how many pins a connector has, and what the function of each pin is.
More generally, design issues here deal with Mechanical, Electrical and Procedural matters.

## Slide 20
Define medium of communication.
Regulates the transmission of a stream of bits over a medium Wired/Wireless.
Transmits bits from one computer to another (Converting bits into signal)
Defines how the cable is attached to the network adapter and what transmission technique is used to send data over the cable. Deals with issues like
  The definition of 0 and 1, e.g. how many volts represents a 1, and how long a bit lasts?
  Whether the channel is simplex or duplex?
  How many pins a connector has, and what the function of each pin is?
Layer 1: Physical Layer
Notes: The Physical Layer is concerned with the details of bit transmission over a physical channel.
Design issues for this layer include:
the definition of 0 and 1, e.g. how many volts represents a 1, and how long a bit lasts,
whether the channel is simplex or duplex,
how many pins a connector has, and what the function of each pin is.
More generally, design issues here deal with Mechanical, Electrical and Procedural matters.

## Slide 21
Protocols:
Encoding techniques
Modulation techniques
Interface Standards
Transmission media
  Wired
  Wireless
The physical layer is also concerned with:
  Bit rate
  Point-to-point, multipoint or point-to-multipoint line configuration
  Physical network topology, for example bus, ring, mesh or star network
  Serial or parallel communication
  Simplex, half duplex or full duplex transmission mode
Layer 1: Physical Layer
Notes: The Physical Layer is concerned with the details of bit transmission over a physical channel.
Design issues for this layer include:
the definition of 0 and 1, e.g. how many volts represents a 1, and how long a bit lasts,
whether the channel is simplex or duplex,
how many pins a connector has, and what the function of each pin is.
More generally, design issues here deal with Mechanical, Electrical and Procedural matters.

## Slide 22
Provides reliable transmission of frames on node to node basis
  Provides frame abstraction (Framing Protocols)
  Provides physical address to the nodes in the network
  Provides Flow Control
    It waits for an acknowledgment from the receiving computer.
    Retransmits frames for which acknowledgement not received
  Provides Error Control
  Provides Medium Access Control
Layer 2: Data Link Layer
Data Link Layer
Logical Link Control Sub layer
Medium Access Control Sub layer
Notes: This layer takes the ‘raw’ transmission facility provided by the Physical Layer (Layer 1) and uses it to provide a reliable, error-free transmission service.
It does this by breaking the data stream up into frames, typically of thousands of bytes in length. Where necessary, special acknowledgement frames can be sent back by the receiving Data Link entity to indicate successful receipt of each frame.
The Physical Layer transmits a continuous sequence of bits, and so Layer 2 must create and recognise frame boundaries. This is typically done by the insertion of special bit patterns.
Channel errors can completely destroy a frame, and hence retransmission may be necessary. This, in turn, leads to the possibility of duplicate frames being received. Data Link protocols must deal with these problems.
A Data Link protocol may offer several different ‘service classes’ to the Network Layer, each with a different quality and cost.
The Data Link Layer must also regulate traffic flow to prevent ‘swamping’ of a slow receiver.
In a duplex channel there may be competition between data and acknowledgment frames; one solution is known as piggybacking, where acknowledgement information is attached to data frames.

## Slide 23
Protocols
  ARP and InARP: Address Resolution Protocol and Inverse ARP.
  RARP: Reverse Address Resolution Protocol
  Stop and Wait Protocol
  Sliding Window Protocol
  PPP
  DDCMP
  IEEE 802.3 onwards
  CRC, Checksum, Hamming Codes…
Layer 2: Data Link Layer
Notes: This layer takes the ‘raw’ transmission facility provided by the Physical Layer (Layer 1) and uses it to provide a reliable, error-free transmission service.
It does this by breaking the data stream up into frames, typically of thousands of bytes in length. Where necessary, special acknowledgement frames can be sent back by the receiving Data Link entity to indicate successful receipt of each frame.
The Physical Layer transmits a continuous sequence of bits, and so Layer 2 must create and recognise frame boundaries. This is typically done by the insertion of special bit patterns.
Channel errors can completely destroy a frame, and hence retransmission may be necessary. This, in turn, leads to the possibility of duplicate frames being received. Data Link protocols must deal with these problems.
A Data Link protocol may offer several different ‘service classes’ to the Network Layer, each with a different quality and cost.
The Data Link Layer must also regulate traffic flow to prevent ‘swamping’ of a slow receiver.
In a duplex channel there may be competition between data and acknowledgment frames; one solution is known as piggybacking, where acknowledgement information is attached to data frames.

## Slide 24
Manages addressing/routing of data within the subnet
  Addresses messages and translates logical addresses and names into physical addresses.
  Determines the route from the source to the destination computer
  Manages traffic problems, such as switching, routing, and controlling the congestion of data packets.
Routing can be:
  Based on static tables
  determined at start of each session
  Individually determined for each packet, reflecting the current network load.
Layer 3: Network Layer
Notes: The Network Layer controls the subnet.
The key design issue is routing of data within the subnet. Routing can be:
based on static tables (rarely changed),
determined at the start of each session, or
highly dynamic: individually determined for each packet, reflecting the current network load.
Too many packets in the subnet simultaneously can form bottlenecks; this is dealt with by congestion control procedures in the Network Layer.
Accounting for subnet use is also typically the responsibility of the Network Layer.
When a packet travels from one network to another, address conversion may be necessary; this is also performed by the Network Layer.
In Broadcast networks (e.g. many LANs), the routing problem is very straightforward, and hence Layer 3 will be very simple, or even non-existent.

## Slide 25
Provides connectionless best effort data delivery services to upper layer protocols
Best effort data delivery services means:
  Packets may follow different path to reach to the destination
  Packet may be lost in the network
  Packet may experience unexpected delay in reaching the destination
  Packets may reach out of order at the destination
Protocols
  IP: Internet Protocol (IPv4)
  IPv6: Internet Protocol version 6
  ICMP & ICMPv6: Internet Message Control Protocol and ICMP version 6
  Mobile IP: IP Mobility Support Protocol for IPv4 & IPv6
  IPSec: IP Security Protocol
Layer 3: Network Layer
Notes: The Network Layer controls the subnet.
The key design issue is routing of data within the subnet. Routing can be:
based on static tables (rarely changed),
determined at the start of each session, or
highly dynamic: individually determined for each packet, reflecting the current network load.
Too many packets in the subnet simultaneously can form bottlenecks; this is dealt with by congestion control procedures in the Network Layer.
Accounting for subnet use is also typically the responsibility of the Network Layer.
When a packet travels from one network to another, address conversion may be necessary; this is also performed by the Network Layer.
In Broadcast networks (e.g. many LANs), the routing problem is very straightforward, and hence Layer 3 will be very simple, or even non-existent.

## Slide 26
OSPF: Open Shortest Path First Protocol (version 2)
RIP: Routing Information Protocol (RIP2)
RIPng: Routing Information Protocol next generation for IPv6
RSVP: Resource Reservation Protocol
BGP: Border Gateway Protocol
Layer 3: Network Layer
Notes: The Network Layer controls the subnet.
The key design issue is routing of data within the subnet. Routing can be:
based on static tables (rarely changed),
determined at the start of each session, or
highly dynamic: individually determined for each packet, reflecting the current network load.
Too many packets in the subnet simultaneously can form bottlenecks; this is dealt with by congestion control procedures in the Network Layer.
Accounting for subnet use is also typically the responsibility of the Network Layer.
When a packet travels from one network to another, address conversion may be necessary; this is also performed by the Network Layer.
In Broadcast networks (e.g. many LANs), the routing problem is very straightforward, and hence Layer 3 will be very simple, or even non-existent.

## Slide 27
Manages transmission packets
  Repackages long messages when necessary into small packets for transmission
  Reassembles packets in correct order to get the original message.
Handles error recognition and recovery.
  Transport layer at receiving acknowledges packet delivery.
  Resends missing packets
  Provides Connection less and Connection Oriented data delivery services
  Provide port number to identify sockets of the connection
Layer 4: Transport Layer
Notes: The basic function of the Transport Layer is to take data from the Session Layer (Layer 5), split it up into smaller units (as necessary), and pass these units on to the Network Layer. It is then also responsible for ensuring that all the pieces are received correctly and reassembled in the correct order.
Typically the Transport Layer will create a distinct Network Layer connection for each Transport connection requested by the Session Layer. However, depending on the data load and the capacity of a single Session channel:
multiple Network connections might be used to support a single high-bandwidth Session connection, or
one high-bandwidth Network connection might be used to support several Session connections.
The Transport Layer also determines what Type of Service to provide to the Session Layer and, ultimately, to the network users. For example:
an error-free, point-to-point channel, guaranteeing data is delivered in the correct order (the most common type of service),
transport of isolated messages with no guarantee of correct ordering, or
message broadcast to multiple destinations
Transport is the first true end-to-end layer, i.e. the Transport protocol communicates between end parties and not to any of the intermediaries.

## Slide 28
Protocols
  TCP: Transmission Control Protocol
  UDP: User Datagram Protocol
  RDP: Reliable Data Protocol
  RUDP: Reliable User Datagram Protocol (Reliable UDP)
Layer 4: Transport Layer
Notes: The basic function of the Transport Layer is to take data from the Session Layer (Layer 5), split it up into smaller units (as necessary), and pass these units on to the Network Layer. It is then also responsible for ensuring that all the pieces are received correctly and reassembled in the correct order.
Typically the Transport Layer will create a distinct Network Layer connection for each Transport connection requested by the Session Layer. However, depending on the data load and the capacity of a single Session channel:
multiple Network connections might be used to support a single high-bandwidth Session connection, or
one high-bandwidth Network connection might be used to support several Session connections.
The Transport Layer also determines what Type of Service to provide to the Session Layer and, ultimately, to the network users. For example:
an error-free, point-to-point channel, guaranteeing data is delivered in the correct order (the most common type of service),
transport of isolated messages with no guarantee of correct ordering, or
message broadcast to multiple destinations
Transport is the first true end-to-end layer, i.e. the Transport protocol communicates between end parties and not to any of the intermediaries.

## Slide 29
Allows two applications on different computers to establish, use, and end a session.
  e.g. file transfer, remote login
Establishes dialog control
  Regulates which side transmits, plus when and how long it transmits.
Performs token management and synchronization.
Protocols:
RPC: Remote Procedure Call Protocol
Layer 5: Session Layer
Notes: The Session Layer allows the establishment of sessions between machines, e.g. to allow remote logins to a multi-user system, or to perform file transfer between machines.
One of the Session services is dialogue control; if the communications are half-duplex then the session layer can manage which entity sends when.
A related service is token management. In some protocols it is essential that both entities do not attempt the same operation simultaneously. Possession of a token permits the operation.
The other main Session service is synchronization. As an example consider attempting a 2-hour file transfer between machines which crash on average once an hour. The synchronization service provides a means for checkpoints to be inserted into the data stream so that, after a crash, only data sent since the last checkpoint needs to be re-transmitted.

## Slide 30
Level at which applications access network services.
  Represents services API
  directly support software applications for file transfers, database access, and electronic mail etc.
  Protocols:
  BOOTP: Bootstrap Protocol,
  DCAP: Data Link Switching Client Access Protocol,
  DHCP: Dynamic Host Configuration Protocol,
  DNS: Domain Name System (Service) Protocol
Layer 7: Application Layer
Notes: The Application Layer is home to a wide variety of protocols to meet specific user needs.
Network virtual terminal. Used by ‘networked screen editors’ and other networked applications needing to handle many different terminal types. Software exists to map the functions of the virtual terminal onto the real terminal, e.g. cursor movement. Examples include OSI VTP and Internet telnet.
File transfer. Different file systems have different file naming conventions and internal record structures. Such a protocol must convert files to a ‘standard’ representation. Examples include OSI FTAM and Internet ftp.
Electronic mail. Examples of electronic mail protocols are OSI X.400 and Internet mail.
Directory service. Examples include OSI X.500.

## Slide 31
Explicit Presentation and session layers missing in Internet Protocols
Data Link and Network Layers redesigned
OSI vs TCP/IP
Application
Presentation
Session
Transport
Network
Data Link
Physical
Application
Transport
Network
Data Link
Physical
Notes: The Physical Layer is concerned with the details of bit transmission over a physical channel.
Design issues for this layer include:
the definition of 0 and 1, e.g. how many volts represents a 1, and how long a bit lasts,
whether the channel is simplex or duplex,
how many pins a connector has, and what the function of each pin is.
More generally, design issues here deal with Mechanical, Electrical and Procedural matters.

## Slide 35
Layers can offer connection-oriented or connectionless services.
Connection-oriented like telephone system Circuit Switching.
Connectionless like postal system Packet Switching.
Each service has an associated Quality-of-service (e.g. reliable or unreliable).
Connections
Notes: Most layers can offer two different types of service:
connection-oriented service, and
connectionless service.
Connection-oriented services are like the telephone system. There are three phases to a connection:
connection establishment (as in picking up the telephone and dialling),
data transfer (conversation), and
connection release (put down the telephone).
Connectionless services are like the postal system. Each message, like a letter, is equipped with the complete address of the recipient, and each message is routed independently. Re-ordering of messages may occur (unlike with a connection-oriented service).
Each service has an associated quality-of-service.

## Slide 36
Reliable services never lose/corrupt data.
Reliable service costs more.
Typical application for reliable service is file transfer.
Typical application not needing reliable service is voice traffic.
Reliability
Notes: Reliable services never lose or corrupt data; to implement a reliable service typically requires the receiver to acknowledge receipt of each part of a message. Hence providing a reliable service has an overhead, and so a choice needs to be made between cheapness and the level of reliability required.
A typical application of a reliable connection-oriented service is file transfer. A recipient of a file will want to be sure that it is correct, even though this may cost more.
Some applications do not need a reliable service, and indeed may not be able to cope with the delays associated with providing one. A simple example is provided by digitised voice traffic, where delay is less tolerable than the occasional burst of noise.

## Slide 37
Protocol = set of rules governing data communication between peer entities, i.e. format and meaning of frames/packets.
Service/protocol decoupling very important.
Protocols
Notes: Services and protocols are two quite distinct things, although they are often confused.
A service consists of a set of primitives (or operations) provided by one layer to the layer above it. The service defines what operations the layer can perform, but says nothing about how they are provided.
By contrast, a protocol is a set of rules governing what is actually transmitted between peer entities, i.e. the format and meaning of frames, packets or messages.
Entities use protocols to implement their service definitions, and are free to change their protocol provided the set of services does not change. That is services and protocols are decoupled.
Many pre-OSI protocols did not make this distinction, e.g. a typical layer might have a service primitive called send packet, referring to a pre-assembled packet of data. This causes great problems when individual protocols need to be replaced.

## Slide 38: Header Encapsulation

## Slide 42: Other Protocols of Interest
VoIP (Voice over IP)
RTP (Real Time Transfer Protocol)
SIP (Session Initiation Protocol)
SSH (Secure Shell)
IGMP (Internet Group Management Protocol)
PPP (Point to Point Protocol)
SLIP (Serial Line Internet Protocol)

## Slide 43
Questions Please?