## Slide 1: Data Link Layer

## Slide 2: Responsibilities of DLL
Provide following services to upper layer protocols:
Logical Link Control Sublayer
  Framing
  Error Control
  Flow Control
  Reliable Transmission
In multipoint network, MAC sublayer will be present after LLC at DLL.
  Medium Access Control

## Slide 3: Network Performance Matrix
Network performance can be measured in two different ways:
  Latency
  Bandwidth (Throughput)
Defn: Network throughput (or effective throughput) is the measured number of bits that can be transmitted over a particular medium in a given amount of time. Usually, described in bits/sec (or bps).
The throughput is the maximum number of bits/sec an application can expect to receive.
Bandwidth >= Throughput
For applications, we can describe throughput as the “bandwidth requirements of an application.”

## Slide 4: Network Performance Matrix
Defn: Latency (or end-to-end delay) is the amount of time is takes for a single bit to propagate from one end of a network to another. It depends upon the following factors:
          Propagation delay
          Transmission time
          Queueing delay
          Processing delays

## Slide 5: Network Performance Matrix
Propagation delay
  We calculate this using the speed-of-light propagation delay:
    in a vacuum, 3.0 * 108 meters/sec
    in a cable, 2.3 *108 meters/sec
    in fiber, 2.0 * 108 meters/sec
  This value is a function of the distances and the speed-of-light delay.
Transmission Delay
  This is the amount of time it takes to transmit the data onto the transmission media. This value is a function of the bandwidth and the packet size.
Queueing Delay
This is the time the data spends in being waiting for its turn (queueing) to be transmitted.
4. Processing Delay
  This is the time the data spends in being processed to be transmitted.

## Slide 6: Latency

## Slide 7: Example
Given the internet pictured below with a propagation speed of 200 m/microsec on the packet-switched WAN and the LAN and:
  nodes 1-4 equidistantly spaced 2 km apart on a WAN with 50 Mbps links between nodes.
  Assume processing time for these nodes is 0.
  nodes A, B, Y, Z and 4 are on a 10BASE5 coaxial LAN with nodes A and Z at the absolute
  edge of the LAN segment and node 4 connected at the middle of the LAN.
  Assume a packet = frame = 1000 bytes on this internet, and no processing delay at any nodes.
How long will it take to send a packet from node 1 to node Z in the situation that when the packet arrives at node 4 there are two packets in front of it waiting to go out on the LAN to Node A.

## Slide 8: Example

## Slide 9: Solution

## Slide 10: Solution

## Slide 11: Framing Protocols
In computer networks, we are operating in a packet switching network which means block of data (not individual bits) are exchanged between the nodes.
Network adapter enables the nodes to exchange frames (block of data).
The problem at the DLL is that how to mark the start of the frame and end of the frame in the bit stream received from the physical later.

## Slide 12: Framing Protocols
Several approached are used to handle this problem:
Framing Protocols
Byte Oriented Approach
Bit Oriented Approach
Sentinel Approach
Sentinel Approach
Byte Counting Approach

## Slide 13: Framing Protocols (Contd.)
Byte-oriented Protocols
  To view each frame as a collection of bytes (characters) rather than bits.
  Sentinel Approach
    BISYNC (Binary Synchronous Communication) Protocol
    Developed by IBM (late 1960)
  Byte Counting Approach
    DDCMP (Digital Data Communication Protocol)
    Used in DECNet

## Slide 14: Framing Protocols (Contd.)
BISYNC – Sentinel Approach (Byte Oriented)
  Frames transmitted beginning with leftmost field
  Beginning of a frame is denoted by sending a special SYN (synchronize) character
  Data portion of the frame is contained between special sentinel character STX (start of text) and ETX (end of text)
  SOH : Start of Header
  DLE : Data Link Escape
  CRC: Cyclic Redundancy Check
BISYNC Frame Format

## Slide 15: Framing Protocols (Contd.)
DDCMP: Byte-counting approach (Byte Oriented)
  count : how many bytes are contained in the frame body
  If count is corrupted
    Framing error
DDCMP Frame Format

## Slide 16: Framing Protocols (Contd.)
Point to Point Protocol (PPP): Sentinel Approach (Bit Oriented)
which is commonly run over Internet links uses sentinel approach
  Special start of text character denoted as Flag
    0 1 1 1 1 1 1 0
  Address, control: default numbers
  Protocol for demux: IP / IPX
  Payload : negotiated (1500 bytes)
  Checksum: for error detection
PPP Frame Format
Specifies what kind of packet is contained in the payload, e.g., LCP, NCP, IP, OSI CLNP, IPX

## Slide 17: HDLC header fields details (Byte Oriented)
Unnumbered frame
All stations are to
accept the frame
Difference between HDLC and PPP is that HDLC is implemented by Point-to-point configuration and also multi-point configurations on the other hand While PPP is implemented by Point-to-Point configuration only.
Flag 01111110 | Address 11111111 | Control 00000011 | Data | CRC | Flag 01111110

## Slide 18: Framing Protocols (Contd.)
Problem with the framing protocols: If the special character appears in between the frame in Byte Oriented Approach.
Solution: Byte Stuffing.
Problem with the framing protocols: If the special bit sequence appears in between the frame in Bit Oriented Approach.
Solution: Bit Stuffing.

## Slide 19: Byte Stuffing
Also referred to as character stuffing.
ASCII characters are used as framing delimiters (e.g. DLE STX and DLE ETX)
The problem occurs when these character patterns occur within the “transparent” data.
Solution: sender stuffs an extra DLE into the data stream just before each occurrence of an “accidental” DLE in the data stream.
The data link layer on the receiving end unstuffs the DLE before giving the data to the network layer.

## Slide 20: Byte Stuffing (Example)
DLE
STX
DLE
ETX
Transparent Data
DLE
STX
DLE
ETX
A
B
DLE
H
W
DLE
STX
DLE
ETX
A
B
DLE
H
W
DLE
DLE
STX
DLE
ETX
A
B
DLE
H
W
Stuffed
Unstuffed
Before

## Slide 21: Bit Stuffing
Each frame begins and ends with a special bit pattern called a flag byte [01111110]. {Note this is 7E in hex}
Whenever sender data link layer encounters five consecutive ones in the data stream, it automatically stuffs a 0 bit into the outgoing stream.
When the receiver sees five consecutive incoming ones followed by a 0 bit, it automatically destuffs the 0 bit before sending the data to the network layer.

## Slide 22: Bit Stuffing (Example)
Input Stream
Stuffed Stream
Unstuffed Stream
0110111111100111110111111111100000
01101111101100111110011111011111000000
0110111111100111110111111111100000
Stuffed bits

## Slide 23: Error Control
It is possible that data may get corrupted during the transmission because of noise, interference etc. This is known as error in the communication.
It is the responsibility of DLL and other higher layer to ensure error free communication.

## Slide 24: Error Control (Contd.)
Error in the communication can be classified as:
  Single Bit Error
  Burst Error
  Burst Error of 6 bits.
0 1 1 0 1 0 1 0
0 1 0 0 1 0 1 0
0 1 1 0 1 0 1 0
0 1 0 0 1 0 1 1

## Slide 25: Error Control (Contd.)
Error Control at DLL
Error Detection Techniques
Error Correction Techniques
Hamming Codes
Parity Check
Checksum
CRC
Hamming Codes

## Slide 26: Error Control (Contd.)
Basic Idea of Error Detection
  To add redundant information to a frame that can be used to determine if errors have been introduced.
  In general, we can provide strong error detection technique
    k redundant bits, n bits message, k << n
    In Ethernet, a frame carrying up to 12,000 bits of data requires only 32-bit CRC.
Parameter of evaluation
  Total number of redundant bits requird.
  Power of error detection / correction.

## Slide 27: Error Control (Contd.)
Extra bits are redundant
  They add no new information to the message
  Derived from the original message using some algorithm
  Both the sender and receiver know the algorithm
  Sender Receiver
Receiver computes r using m bits. If they match, no error else data received has error.
m
r
m
r

## Slide 28: Parity Check (One dimensional parity)
Algo:
  Divide the message into words (7 bit word, 15 bit word, 31 bit word etc.)
  Append a single parity bit at the end to the sequence of message bits.
    Odd Parity: The parity bit is chosen to make the total number of 1’s in the message odd.
    Even Parity: The parity bit is chosen to make the total number of 1’s in the message even.
    Example of even parity: Green bit is the parity bit
    Number of redundant bit required is very high.
    Power of error detection: Can detect if odd number of bits are involved in the error.
0 1 1 0 1 0 1 0
0 1 0 0 1 0 1 0

## Slide 29: Two-dimensional parity check
Two-dimensional parity is exactly what the name suggests
  Two-dimensional parity does a similar calculation for each bit position across each of the bytes contained in the frame
  This results in an extra parity byte for the entire frame, in addition to a parity bit for each byte.

## Slide 30: Two-dimensional parity check
Two Dimensional Parity
Number of redundant bits required is very high.
Two-dimensional parity catches all 1-, 2-, and 3-bit errors and most 4-bit errors.

## Slide 31: Checksum
Transmitter’s Algo:
  1’s complement arithmetic is used for implementation.
  Divide the message into words. (8 / 16 / 32 bit words).
  Calculate the sum of all the units using 1’s complement arithmetic.
  Take ones complement of the result. This is called the checksum.
  Transmit the checksum along with the message.
Receiver’s Algo:
  Divide the message into words including the checksum. (8 / 16 / 32 bit words).
  Calculate the sum of all the units using 1’s complement arithmetic.
  Take ones complement of the result.
  If the result is all zero then accept else discard.

## Slide 32: 1’s Complement Arithmetic
In ones complement arithmetic, a negative integer −x is represented as the complement of x;
  Each bit of x is inverted.
When adding numbers in ones complement arithmetic, a carryout from the most significant bit needs to be added to the result.

## Slide 33: Example of decimal representation

## Slide 34: Checksum Example
Consider, for example, the addition of −5 and −3 in ones complement arithmetic on 4-bit integers
  +5 is 0101, so −5 is 1010; +3 is 0011, so −3 is 1100
If we add 1010 and 1100 ignoring the carry, we get 0110.
In ones complement arithmetic, the fact that this operation caused a carry from the most significant bit causes us to increment the result, giving 0111, which is the ones complement representation of −8 (obtained by inverting the bits in 1000), as we would expect.
At receiver’s end If we add 1010, 1100 and 1000 we get 1111 as sum.
Complement of 1111 is 0000. Which means there is no error in the transmission.

## Slide 35: Checksum Example
Sender’s Side Receiver’s Side
0001
f203
f4f5
f6f7
+(0000)
------
2ddf0
ddf0
+ 2
------
ddf2
220d
0001
f203
f4f5
f6f7
+ 220d
------
2fffd
fffd
+ 2
------
ffff
0000

## Slide 36: Checksum Properties
Number of redundant bits are constant and will depends on the word size chosen.
It can detect all the errors where odd number of bits are involved in the error, most of the 2-bits and most of the 4-bits errors.

## Slide 37: Cycle Redundancy Check (CRC)
Reduce the number of extra bits and maximize protection.
CRC uses a special class of polynomial arithmetic known as “Polynomial Arithmetic Modulo 2”.
For the purpose of implementation following properties of Polynomial Arithmetic Modulo 2 are important:

## Slide 38: Cycle Redundancy Check (CRC)

## Slide 39: Cycle Redundancy Check (CRC)
Sender’s Algorithm:
Let r be the degree of code polynomial can call it c(x) (Both sender and receiver know it)
Append r zero bits at the end of message bits and call it S(x).
Divide S(x) by C(x) using modulo 2 division to get the remainder R(x).
Subtract R(x) from S(x) and call it T(x).
Transmit T(x).

## Slide 40: Cycle Redundancy Check (CRC)
Receiver’s Algorithm:
Let receiver receive a message and call it M(x).
Divide M(x) by C(x) to get remainder R(x).
If R(x) = 0 then accept else discard.

## Slide 41: Example (Sender Side)
At Sender:
Let M = 1 1 0 0 →
Let C(x) = x3 + x + 1 →C=1 0 1 1; Degree of C(x) = 3
Division:
x3 + x + 1 ) x6 + x5
x3 + x2 + x
x6 + x4 + x3
x5 + x4 + x3
x5 + x3 + x2
x4 + x2
x4 + x2 + x
x
= q(x) quotient
= r(x) remainder = 010
divisor
dividend
35 ) 122
3
105
17

## Slide 42: Example (Receiver Side)
At receiver suppose M(x) = 1 1 0 0 0 0 0
C(x) = 1 0 1 1
R(x) = 100
=> error in the data received therefore, discard the frame.

## Slide 43: CRC Properties
Properties of Generator Polynomial
  Let P(x) represent what the sender sent and P(x) + E(x) is the received string. A 1 in E(x) represents that in the corresponding position in P(x) the message the bit is flipped.
  We know that P(x)/C(x) leaves a remainder of 0, but if E(x)/C(x) leaves a remainder of 0, then either E(x) = 0 or C(x) is factor of E(x).
  When C(x) is a factor of E(x) we have problem; errors go unnoticed.
  If there is a single bit error then E(x) = xi, where i determines the bit in error. If C(x) contains two or more terms it will never divide E(x), so all single bit errors will be detected.
  Therefore it is important to use code polynomial which satisfy the above properties and maximize the error detection power.

## Slide 44: Standard Polynomials used for CRC
Six generator polynomials that have become international standards are:
  CRC-8 = x8+x2+x+1
  CRC-10 = x10+x9+x5+x4+x+1
  CRC-12 = x12+x11+x3+x2+x+1
  CRC-16 = x16+x15+x2+1
  CRC-CCITT = x16+x12+x5+1
  CRC-32 = x32+x26+x23+x22+x16+x12+x11+x10+x8+x7+x5+x4+x2+x+1

## Slide 45: CRC Properties
  In general, it is possible to prove that the following types of errors can be detected by a C(x) with the stated properties:
    All single-bit errors, as long as the xk and x0 terms have nonzero coefficients.
    All double-bit errors, as long as C(x) has a factor with at least three terms.
    Any odd number of errors, as long as C(x) contains the factor (x+1).
    Any “burst” error (i.e., sequence of consecutive error bits) for which the length of the burst is less than k bits. (Most burst errors of larger than k bits can also be detected.)

## Slide 46: Error Correction Technique
Also known as forward error correction (FEC).
FEC is used in transmission of radio signals, such as those used in transmission of digital television (Reed-Solomon and Trellis encoding) and 4D-PAM5 (Viterbi and Trellis encoding).
Some FEC is based on Hamming Codes

## Slide 47: Hamming Codes (for 1 bit error correction)
Suppose the message consists of m bits and number of redundant bits r, required to implement the Hamming Code algorithm.
How large does r need to be can be calculated by satisfying the following equality for the minimum value of r.

## Slide 48: Sender’s Algorithm
Bits are numbered from left to right from 1 to m+r.
Power of 2 bit positions are reserved for redundant bits.
Remaining bit position are filled with message bits.
Each redundant bit will force a parity (even or odd) on the subset of message bits.

## Slide 49: Sender’s Algorithm
Each data bit is included in a unique set of parity bits, as determined its bit position in binary form. a. Parity bit 1 covers all the bits positions whose binary representation includes a 1 in the least significant position (1, 3, 5, 7, 9, 11, etc). b. Parity bit 2 covers all the bits positions whose binary representation includes a 1 in the second position from the least significant bit (2, 3, 6, 7, 10, 11, etc). c. Parity bit 4 covers all the bits positions whose binary representation includes a 1 in the third position from the least significant bit (4–7, 12–15, 20–23, etc).

## Slide 50: Sender’s Algorithm
d. Parity bit 8 covers all the bits positions whose binary representation includes a 1 in the fourth position from the least significant bit bits (8–15, 24–31, 40–47, etc). e. In general, each parity bit covers all bits where the bitwise AND of the parity position and the bit position is non-zero.
Since we check for even parity set a parity bit to 1 if the total number of ones in the positions it checks is odd.
Set a parity bit to 0 if the total number of ones in the positions it checks is even.

## Slide 51: Determination of Subset

## Slide 52: Example
m=1011
r=3
m+r = 7
 |  | 1 |  | 0 | 1 | 1
r1 | r2 | d1 | r3 | d2 | d3 | d4
1 | 2 | 3 | 4 | 5 | 6 | 7

## Slide 53: Subset of r1= 1, 3, 5, 7 Subset of r2 = 2, 3, 6, 7 Subset of r3 = 4, 5, 6, 7
Decimal Value | r3 | r2 | r1
1 | 0 | 0 | 1
2 | 0 | 1 | 0
3 | 0 | 1 | 1
4 | 1 | 0 | 0
5 | 1 | 0 | 1
6 | 1 | 1 | 0
7 | 1 | 1 | 1
Decimal Value | r3 | r2 | r1
1 | 0 | 0 | 1
2 | 0 | 1 | 0
3 | 0 | 1 | 1
4 | 1 | 0 | 0
5 | 1 | 0 | 1
6 | 1 | 1 | 0
7 | 1 | 1 | 1

## Slide 54: Example
For implementing odd parity
r1 = 1
r2= 0
r3= 1
T(x) = 1 0 1 1 0 1 1

## Slide 55: Receiver’s Algorithm
If the parity is satisfied on the subsets then fill 1 in the table otherwise 0. The decimal equivalent of that binary value will give the position of error.
For example suppose the received message =1 0 1 1 0 0 1
0 1 0 => 2 is the position of error.
Evaluation of parity of corresponding subset of redundant bits | r3 | r2 | r1
 | 0 | 1 | 0
Evaluation of parity of corresponding subset of redundant bits | r3 | r2 | r1
 | 0 | 1 | 0