## Slide 1: Wireless Security
S.Venkatesan
Indian Institute of Information Technology, Allahabad

## Slide 2: Slides from
Sandeep Kumar Shukla, IIT Kanpur

## Slide 3: WLAN Security - Contents
Wireless LAN 802.11
Technology
Vulnerabilities

## Slide 4: Wireless LANs
IEEE ratified 802.11 in 1997.
  Also known as Wi-Fi.
Wireless LAN at 1 Mbps & 2 Mbps.
WECA (Wireless Ethernet Compatibility Alliance) promoted Interoperability.
  Now Wi-Fi Alliance
802.11 focuses on Layer 1 & Layer 2 of OSI model.
  Physical layer
  Data link layer

## Slide 5: 802.11 Components
Two pieces of equipment defined:
  Wireless station
    A desktop or laptop PC or PDA with a wireless NIC.
  Access point
    A bridge between wireless and wired networks
    Composed of
      Radio
      Wired network interface (usually 802.3)
      Bridging software
    Aggregates access for multiple wireless stations to wired network.

## Slide 6: 802.11 modes
Infrastructure mode (BSS)
  Basic Service Set
    One access point
  Extended Service Set (ESS)
    Two or more BSSs forming a single subnet.
  Most corporate LANs in this mode.
Ad-hoc mode
  Also called peer-to-peer.
  Independent Basic Service Set
  Set of 802.11 wireless stations that communicate directly without an access point.
    Useful for quick & easy wireless networks.

## Slide 7: Infrastructure mode
Basic Service Set (BSS) –
Single cell
Extended Service Set (ESS) –
Multiple cells
Access Point
Station
Notes: Usual configuration for offices.

## Slide 8: Ad-hoc mode
Independent Basic Service Set (IBSS)
Notes: For meetings, conferences or other places where wireless infrastructure (access points) doesn’t exist.

## Slide 9: 802.11 Physical Layer
Originally three alternative physical layers
  Two incompatible spread-spectrum radio in 2.4Ghz ISM band
    Frequency Hopping Spread Spectrum (FHSS)
      75 channels
    Direct Sequence Spread Spectrum (DSSS)
      14 channels (11 channels in US)
  One diffuse infrared layer
802.11 speed
  1 Mbps or 2 Mbps.
Notes: Industrial, Scientific and Medi
In telecommunications, direct-sequence spread spectrum (DSSS) is a spread-spectrum modulation technique primarily used to reduce overall signal interference. The direct-sequence modulation makes the transmitted signal wider in bandwidth than the information bandwidth. After the despreading or removal of the direct-sequence modulation in the receiver, the information bandwidth is restored, while the unintentional and intentional interference is substantially reduced.[1]
With DSSS, the message bits are modulated by a pseudorandom bit sequence known as a spreading sequence. Each spreading-sequence bit, which is known as a chip, has a much shorter duration (larger bandwidth) than the original message bits. The modulation of the message bits scrambles and spreads the pieces of data, and thereby results in a bandwidth size nearly identical to that of the spreading sequence. The smaller the chip duration, the larger the bandwidth of the resulting DSSS signal; more bandwidth multiplexed to the message signal results in better resistance against interference.[1][2]
Some practical and effective uses of DSSS include the code-division multiple access (CDMA) method, the IEEE 802.11b specification used in Wi-Fi networks, and the Global Positioning System.[3][4]
cal band.

## Slide 10: 802.11 Data Link Layer
Layer 2 split into:
  Logical Link Control (LLC).
  Media Access Control (MAC).
LLC - same 48-bit addresses as 802.3.
MAC - CSMA/CD not possible.
  Can’t listen for collision while transmitting.
CSMA/CA – Collision Avoidance.
  Sender waits for clear air, waits random time, then sends data.
  Receiver sends explicit ACK when data arrives intact.
  Also handles interference.
  But adds overhead.
802.11 always slower than equivalent 802.3.
Notes: Layer 2 split.
LLC has same 48-bit addressing as Ethernet.
Because this is a radio medium, can’t always listen for coliisions while transmitting. Therefore need a way to avoid collisions, instead of detecting collisions.

## Slide 11: Hidden nodes
request-to-send/clear-to-send (RTS/CTS) handshaking (IEEE 802.11 RTS/CTS)
Notes: In the example above, each station can transmit and receive from the access point.
But each station cannot transmit and receive directly to the other station. Reasons may be interference or range. As a result, each station is hidden from the other.
However the access point can see both stations.
Hidden nodes in a wireless network are nodes that are out of range of other nodes or a collection of nodes. Consider a physical star topology with an access point with many nodes surrounding it in a circular fashion: each node is within communication range of the AP, but the nodes cannot communicate with each other.
For example, in a wireless network, it is likely that the node at the far edge of the access point's range, which is known as A, can see the access point, but it is unlikely that the same node can communicate with a node on the opposite end of the access point's range, C. These nodes are known as hidden.
Another example would be where A and C are either side of an obstacle that reflects or strongly absorbs radio waves, but nevertheless they can both still see the same AP.
The problem is when nodes A and C start to send packets simultaneously to the access point B. Because the nodes A and C cannot receive each other's signals, so they cannot detect the collision before or while transmitting, Carrier sense multiple access with collision detection (CSMA/CD) does not work, and collisions occur, which then corrupt the data received by the access point.
To overcome the hidden node problem, request-to-send/clear-to-send (RTS/CTS) handshaking (IEEE 802.11 RTS/CTS) is implemented at the Access Point in conjunction with the Carrier sense multiple access with collision avoidance (CSMA/CA) scheme. The same problem exists in a mobile ad hoc network (MANET).
IEEE 802.11 uses 802.11 RTS/CTS acknowledgment and handshake packets to partly overcome the hidden node problem. RTS/CTS is not a complete solution and may decrease throughput even further, but adaptive acknowledgements from the base station can help too.
The comparison with hidden stations shows that RTS/CTS packages in each traffic class are profitable (even with short audio frames, which cause a high overhead on RTS/CTS frames).[2]
In the experimental environment following traffic classes are included: data (not time critical), data (time critical), video, audio. Examples for notations: (0|0|0|2) means 2 audio stations; (1|1|2|0) means 1 data station (not time critical), 1 data station (time critical), 2 video stations.
Benchmarks: Net Throughput with/without RTS/CTS (Pommer, p.179)
The other methods that can be employed to solve hidden node problem are :
Increase Transmitting Power From the Nodes
Use omnidirectional antennas
Remove obstacles
Move the node
Use protocol enhancement software
Use antenna diversity

## Slide 12: RTS / CTS
To handle hidden nodes
Sending station sends
  “Request to Send”
Access point responds with
  “Clear to Send”
  All other stations hear this and delay any transmissions.
Only used for larger pieces of data.
  When retransmission may waste significant time.
Notes: To handle the problem of hidden nodes or stations that cannot see each other, but can see a common access point,

## Slide 13: 802.11b
802.11b ratified in 1999 adding 5.5 Mbps and 11 Mbps.
DSSS as physical layer.
  11 channels (3 non-overlapping)
Dynamic rate shifting.
    Transparent to higher layers
    Ideally 11 Mbps.
    Shifts down through 5.5 Mbps, 2 Mbps to 1 Mbps.
      Higher ranges.
      Interference.
    Shifts back up when possible.
Maximum specified range 100 metres
Average throughput of 4Mbps
Notes: In telecommunication and radio communication, spread-spectrum techniques are methods by which a signal (e.g., an electrical, electromagnetic, or acoustic signal) generated with a particular bandwidth is deliberately spread in the frequency domain, resulting in a signal with a wider bandwidth. These techniques are used for a variety of reasons, including the establishment of secure communications, increasing resistance to natural interference, noise, and jamming, to prevent detection, to limit power flux density (e.g., in satellite down links), and to enable multiple-access communications.
In telecommunications, direct-sequence spread spectrum (DSSS) is a spread-spectrum modulation technique primarily used to reduce overall signal interference. The direct-sequence modulation makes the transmitted signal wider in bandwidth than the information bandwidth. After the despreading or removal of the direct-sequence modulation in the receiver, the information bandwidth is restored, while the unintentional and intentional interference is substantially reduced.[1]
With DSSS, the message bits are modulated by a pseudorandom bit sequence known as a spreading sequence. Each spreading-sequence bit, which is known as a chip, has a much shorter duration (larger bandwidth) than the original message bits. The modulation of the message bits scrambles and spreads the pieces of data, and thereby results in a bandwidth size nearly identical to that of the spreading sequence. The smaller the chip duration, the larger the bandwidth of the resulting DSSS signal; more bandwidth multiplexed to the message signal results in better resistance against interference.[1][2]
Some practical and effective uses of DSSS include the code-division multiple access (CDMA) method, the IEEE 802.11b specification used in Wi-Fi networks, and the Global Positioning System.[3][4]
Dynamic Rate Switching refers to the tendency of wireless stations to negotiate at different data rates depending on the quality of the received signal from the access point (AP). While essentially important, an unfortunate side effect to Dynamic Rate Switching occurs when clients choose to remain connected to the AP at lower Data Rates rather than roam to an AP with better signal quality.
As the client moves farther away from the center of the wireless cell, the received signal quality worsens, compelling the client station to negotiate at slower data rates to reduce the chance of errors in received errors. Although Dynamic Rate Switching is described from the perspective of the client station, AP radios also shift their data rates depending on the signal received from the active clients.

## Slide 14: Joining a BSS
When 802.11 client enters range of one or more APs
  APs send beacons.
  AP beacon can include SSID.
  AP chosen on signal strength and observed error rates.
  After AP accepts client.
    Client tunes to AP channel.
Periodically, all channels surveyed.
  To check for stronger or more reliable APs.
  If found, reassociates with new AP.
Notes: Wireless NICs can measure strength of wireless signal.

## Slide 15: Access Point Roaming
Channel 4
Channel 7
Channel 9
Channel 1

## Slide 16: Roaming and Channels
Reassociation with APs
  Moving out of range.
  High error rates.
  High network traffic.
    Allows load balancing.
Each AP has a channel.
  14 partially overlapping channels.
  Only three channels that have no overlap.
    Best for multicell coverage.

## Slide 17: 802.11a
802.11a ratified in 2001
The 802.11a amendment to the original standard was ratified in 1999.
Supports up to 54Mbps in 5 Ghz range.
  Higher frequency limits the range
  Regulated frequency reduces interference from other devices
12 non-overlapping channels
Usable range of 30 metres
Average throughput of 30 Mbps
Not backwards compatible

## Slide 18: 802.11g
802.11g ratified in 2002
Supports up to 54Mbps in 2.4Ghz range.
  Backwards compatible with 802.11b
3 non-overlapping channels
Range similar to 802.11b
Average throughput of 30 Mbps
802.11n of 2009
  72 Mbps with MIMO technology, broader spectrum, and Frame aggregation
802.11k, 802.11r, 802.11y, and 802.11w further amends 802.11n

## Slide 19: Open System Authentication
Service Set Identifier (SSID)
Station must specify SSID to Access Point when requesting association.
Multiple APs with same SSID form Extended Service Set.
APs can broadcast their SSID.
Some clients allow * as SSID.
  Associates with strongest AP regardless of SSID.

## Slide 20: MAC ACLs and SSID hiding
Access points have Access Control Lists (ACL).
ACL is list of allowed MAC addresses.
  E.g. Allow access to:
    00:01:42:0E:12:1F
    00:01:42:F1:72:AE
    00:01:42:4F:E2:01
But MAC addresses are sniffable and spoofable.
AP Beacons without SSID
  Essid_jack
    sends deauthenticate frames to client
    SSID then displayed when client sends reauthenticate frames

## Slide 21: Interception Range
Station outside
building perimeter.
Basic Service Set (BSS) –
Single cell
100 metres

## Slide 22: Interception
Wireless LAN uses radio signal.
Not limited to physical building.
Signal is weakened by:
  Walls
  Floors
  Interference
Directional antenna allows interception over longer distances.

## Slide 23: WarDriving
Software
  Netstumbler
  And many more
Laptop
802.11b,g or a PC card
Optional:
  Global Positioning System
  Car, bicycle, boat…
Logging of MAC address, network name, SSID, manufacturer, channel, signal strength, noise (GPS - location).

## Slide 24: Common Attacks on WLAN
Rogue Wireless Devices
Peer-to-Peer Attacks
Eavesdropping
Encryption Cracking
KRACK – Key Reinstallation Attack
Authentication Attack
MAC Spoofing
Wireless Hijack – Evil Twin
DOS Attacks
Vendor Specific Attacks
Social Engineering

## Slide 25: Why do hackers attack WLAN?
Gain Access to Wireless Access points. WLAN Controllers
  These bridge the Wired Network and Wireless
  Getting Access to these lead to access to all Network resources
Privacy Breach of Stations and Users
Decrypt information such as password, credit card information in wireless Frames
Disruption (DOS)
Installation of Rootkit and other Malware

## Slide 26: Rogue Wireless Devices

## Slide 27: Rogue Wireless Devices
Often done by employees for convenience at the cost of security
A Client Device may have two NIC (wired and wireless)]
  Accidentally or intentionally a device connected to wired data port may have a software running to work as AP on wireless NIC

## Slide 28: Peer-to-Peer Attacks
802.11 clients can work either in infrastructure mode or ad hoc mode
Ad hoc mode – IBSS (Independent BSS)
Connecting to IBSS of a device may lead the new device access resources in the device working as access point
Devices connected to the same BSS may also have the same kind of problem unless the AP of the BSS or VLAN do client isolation
Client Isolation – Aps can be configured to block wireless clients from communicating with each other through the AP
  AP won’t forward frame arriving from one client to another
  Also called PSPF – Public Secure Packet Forwarding

## Slide 29: Client Isolation
Some applications like VoWiFi may not work

## Slide 30: Eavesdropping
In absence of strong encryption anyone can listen within range
Casual eavesdropping – WLAN Discovery Tools use
  Finding open WLAN networks
  Listening to AP beacons -- Passive scanning
  Searching for an AP –- active scanning
  Beacon management Frames have information on (in clear text)
    SSID
    MAC Addresses
    Supported data rates
    Other BSS capabilities

## Slide 31: Eavesdropping
  Active Scanning by sending probe request frames
    Probe response frame has same info as a beacon frame
    A probe request without SSID is a null probe request
      All APs respond
  Active scanning WLAN discovery tools often do null probe request
    Such a tool inSSIDer –see www.metageek.net
  Wardriving
    NetStumbler tool – outdated
    WiFi Analyzer (Android based) bit.ly/WIFIAnalyze
    Acrylic WIFI www.acrylicwifi.com
    Wifi heatmap – www.wigle.net
  Protocol Analyzer – captures 802.11 frame transmissions
    Wireshark
    Omnipeek

## Slide 32: Encryption Cracking
WEP compromised over a decade ago (in less than 5 mins)
  Needs several hundred thousand encrypted packets and then use WEP-cracking software
  Derives 40-bit or 104-bit key
KRACK Attack – Key Reinstallation Attack
  www.krackattacks.com
  Requires firmware patches
  Exploits message 3 retransmission in 4-way handshake of WPA2

## Slide 33: Authentication Attacks
Authentication leads to authorization to use network resources
Authentication solutions – 802.1X/EAP or PSK
802.11-2016 does not specify what type of EAP to use
  LEAP – Lightweight Extensible Authentication Protocol
    Offline dictionary attack
    Hashed password response is crackable using dictionary attack
    Capture frames of LEAP authentication to submit to cracker
    After password cracked, username is in plain text – so attacker can authenticate himself to the WLAN
  WLAN infrastructure needs to be secured with 802.1X/EAP solution that uses a RADIUS server and Tunneled authentication EAP (to be discussed later)
  PSK (Preshared Key) used in home Wifi are not as secure – as social engineering may be used to know the pass phrase or dictionary attacks may be used
    Use complex and long passphrase for your home wifi

## Slide 34: MAC Spoofing & Management Interface Exploits
Many APs or WLAN controllers whitelist MAC addresses
  MAC can be spoofed
  Thus MAC filtering is a weak security solution
Management Interface Exploits
  AP, WLAN controllers have a management interface
    Http based, CLI based, serial port connection, SNMP based etc
    Unless strong passwords, and encrypted login capabilities such as SSH2, or HTTPs used – can be compromised
    Once attacker is in management console
      Can change passphrase to lock out users
      Change firmware
      Brick the AP or device
    Suggestion: Always access the management interface through the wired side of the network

## Slide 35: Wireless Hijacking (Evil-Twin)

## Slide 36: DoS, Implementation Vulnerabilities, and Social Engineering
Layer 1 DOS
  Jamming Attacks
Layer 2 DOS
  Manipulation of 802.11 frames
  Disassociation or deauthentication frame can be spoofed
  802.11w-2009 defined management frame protection mechanism (MFP)
    Robust management frames cannot be spoofed
Implementation attacks
  Firmware security bugs need to be patched
Any static information is subject to social engineering
  WEP key , WPA/WPA2-Personal PSK, passphrase etc